## Slide 2
Essentials of Fire Fighting
6th Edition
Firefighter I
Chapter 7 — Portable Fire Extinguishers

## Slide 3: Learning Objective 1
Explain portable fire extinguisher classifications.

## Slide 4: Portable fire extinguishers are chosen based on the type of fuel burning.
Class A
Class B
Class C
Class D
Class K

## Slide 5: Class A fires involve ordinary combustibles.
Fuel
Textiles
Paper
Plastics
Rubber
Wood
Extinguished with:
Water
Water-based agents (Class A foam)
Dry Chemicals

## Slide 6: Class B fires involve flammable, combustible liquids and gases.
Fuel
Alcohol
Gasoline
Lubricating Oils
Liquefied petroleum gas (LPG)
Extinguished with:
Carbon Dioxide
Dry Chemicals
Class B Foam

## Slide 7: Class C fire involves energized electrical equipment.
Treat as Class A or B once power is off

## Slide 8: Class D fires involve combustible metals and alloys.
Lithium
Magnesium
Potassium
Sodium

## Slide 9: CAUTION!
The use of water or water-based agents on Class D fires will cause the fire to react violently, emit bits of molten metal, and possibly injure firefighters close by.

## Slide 10: Use dry powder, not dry chemical, extinguishers on Class D fires.
Dry powder
Dry chemical

## Slide 11: CAUTION!
Do not use a dry chemical extinguisher on Class D fire. The dry chemical often reacts violently with burning metals.

## Slide 12: Class K fires involve combustible cooking oils.
Vegetable or animal fats
Burn at extreme temperatures
Found at commercial, institutional, industrial, home
Controlled by wet chemical systems, portable extinguishers

## Slide 13: REVIEW QUESTION
How are the classifications for portable fire extinguishers divided?

## Slide 14: Learning Objective 2
Describe types of portable fire extinguishers.

## Slide 15: Fire extinguishers are organized by type of extinguishing agent and the method used to expel their contents.
Extinguishing agent
Cooling – Reduces temperature
Smothering – Excludes oxygen
Chain breaking – Interrupts chemical chain reaction
Saponification – Forms oxygen-excluding foam
(Cont.)

## Slide 16: Fire extinguishes are organized by type of extinguishing agent and the method used to expel their contents.
Manual pump – Physical pressure forces agent out nozzle
Stored pressure – Compressed air or inert gas forces agent out nozzle
Pressure cartridge – External expellant forces agent out nozzle when introduced to container
Mechanisms to expel

## Slide 17
Use pump-type water extinguishers on small Class A fires, ground cover fires.

## Slide 18: Use stored-pressure water extinguishers on small Class A fires.

## Slide 19: Use water-mist stored-pressure extinguishers on Class C fires.
Deionized water
Normal water
Water-mist stored-pressure
Stored-pressure water

## Slide 20: Use wet chemical stored-pressure extinguishers on Class K fires.
Potassium based, low pH
Saponification
Courtesy of Ron Moore/McKinney (TX) FD

## Slide 21: Use aqueous film forming foam (AFFF) extinguishers on Class B fires, small fuel spills.

## Slide 22: Clean agent extinguishers replaced halogenated agents.
Rapidly evaporating liquid that leaves no residue
Cools, smothers Class A and B fires
Nonconductive, safe on energized electrical equipment
Courtesy of Ansul Corp.

## Slide 23: REVIEW QUESTION
What are the differences between wet chemical stored-pressure, aqueous film forming foam (AFFF), and clean agent extinguishers?

## Slide 24: Carbon dioxide (CO2) extinguishers discharge as a gas and are most effective on Class B and C fires.
Have limited reach
Easily dispersed by wind
No freeze protection required

## Slide 25: CO2 is stored under its own pressure and is discharged through a plastic or rubber horn.
O2
CO2
Dry ice crystals
Smothers fire
Little cooling effect
Reignition possible

## Slide 26: CAUTION!
When carbon dioxide is discharged, a static electrical charge builds up on the discharge horn. Touching the horn before the charge has dissipated can result in a shock.

## Slide 27: Operate wheeled (CO2) extinguishers in the same manner as handhelds.
Courtesy of Badger Fire Protection
Commonly found in airports and industrial facilities

## Slide 28: Dry chemical extinguishers use additives to keep extinguishing agents ready for use, even after long storage periods.
Regular
B:C rated
Multipurpose
A:B:C rated

## Slide 29: Dry chemical extinguishers may react chemically with other types of extinguishing agents.
Dry chemical
Other agents

## Slide 30: WARNING!
Never mix or contaminate dry chemicals with any other type of agent.

## Slide 31: Dry chemical agents are considered nontoxic and safe for use.
May reduce visibility
May create respiratory problems
May not be compatible with foam

## Slide 32: Follow these steps when using dry chemical extinguishers on Class A fires.
1. Direct discharge to cover with chemical
2. After flames knocked down, apply to smoldering area

## Slide 33: Handheld dry chemical extinguishers come in two basic designs.
Cartridge- operated
Pressure cartridge connected
Tank not pressurized until plunger pushed
Stored pressure
Similar to air-pressurized water
Constant pressure around 200 psi (1 400 kPa)

## Slide 34: CAUTION!
When pressurizing a cartridge-type extinguisher, do not place your head or any other part of your body above the top of the extinguisher. If the fill cap was not properly screwed back on, the cap and/or a cloud of agent can be forcibly discharged.

## Slide 35: Wheeled dry chemical extinguishers operate in a similar manner as handheld cartridge-types.
Agent
Pressurizing gas
Stretch out hose completely;
powder can clog
Allow few seconds to pressurize
after introducing gas
Prepare for significant
nozzle reaction

## Slide 36: CAUTION!
The top of the extinguisher should be pointed away from the operator and any other nearby personnel when pressurizing the unit.

## Slide 37: Use dry powder extinguishers on fires for Class D metals.
No single agent works on all metals
Comes in several models
Consult manufacturer’s guide
Apply with extinguisher or scoop

## Slide 38: Dry powder creates a smothering blanket over burning area.
Apply sufficient depth
Apply gently; do not break crust
Avoid scattering

## Slide 39: CAUTION!
Water applied to a combustible metal fire results in a violent reaction that intensifies the combustion and causes bits of molten material to spatter in every direction.

## Slide 40: Follow these steps if burning metal is on a combustible surface.
1. Cover fire with powder
2. Create layer of powder nearby, 1-2 inches (25-50 mm) deep
3. Spread nearby – Add more as needed
4. Leave undisturbed until completely cool

## Slide 41: REVIEW QUESTION
How do carbon dioxide (CO2), dry chemical, and dry powder extinguishers differ?