## Slide 2
Essentials of Fire Fighting
6th Edition
Firefighter I
Chapter 8 — Ropes, Webbing, and Knots

## Slide 3: Learning Objective 1
Compare and contrast the characteristics of life safety rope and utility rope.

## Slide 4: Fire service rope is divided into two classifications.
Life safety rope
Utility rope
Courtesy of Shad Cooper/Wyoming
State Fire Marshal’s Office

## Slide 5: NFPA® 1983 classifies two additional types of ropes used in rescue.
Escape rope
Water rescue throw line

## Slide 6: NFPA® 1983 sets requirements and regulations for life safety rope.
Continuous filament virgin fiber
Required manufacturer information
Block creel construction
For load-bearing elements
(Cont.)

## Slide 7: NFPA® 1983 sets requirements and regulations for life safety rope.
Criteria for re-use
Requires rope log
Designates options for rope removed from service

## Slide 8: While NFPA® does not regulate utility rope it should be inspected regularly.

## Slide 9: Synthetic and natural fiber rope are constructed from different materials.
Material effects use, longevity
Natural fiber weakens when wet, rots
Replaced with synthetic

## Slide 10: Synthetic fiber ropes are made from a variety of materials and have many advantages and disadvantages.
- Resistance to water, mildew, mold, rotting, shrinkage, ultraviolet (UV) light
- Melts when exposed to heat
- Long lifespan
- Strong/lightweight
- Easy maintenance

## Slide 11: Natural fiber ropes have distinct advantages and disadvantages.
- Resistant to sunlight
- Mildew/mold
- Does not melt
- Holds knot firmly
- Exposure to chemicals
- Burns in contact with flame, embers

## Slide 12: REVIEW QUESTION
What are the differences in the characteristics of life safety and utility rope?

## Slide 13: Use only kernmantle rope construction for life safety operations.

## Slide 14: Kernmantle rope is made of synthetic material and consists of two main components.
Braided covering or sheath (mantle)
Core (kern) of main load- bearing strands

## Slide 15: Kernmantle rope can be either dynamic or static and should be used in different circumstances.
Dynamic rope
Static rope

## Slide 16: Laid (twisted) rope can be either synthetic or natural and is used only for utility rope.
Courtesy of Shad Cooper/Wyoming
State Fire Marshal’s Office
Easy to inspect
- Abrasion, physical damage
- Damage affects strength

## Slide 17: Braided rope is less likely to twist than laid rope, but is still vulnerable.
Courtesy of Shad Cooper/Wyoming
State Fire Marshal’s Office

## Slide 18: Braid-on-braid (double braided) is often confused with kernmantle.
Kernmantle
Braid-on-braid

## Slide 19: Learning Objective 2
Summarize basic guidelines for rope maintenance.

## Slide 20: Learning Objective 3
Explain reasons for placing rope out of service.

## Slide 21: Four aspects of maintenance help keep rope ready to use when needed.
Inspect
Clean
Store
Care for

## Slide 22: All rope must be inspected after use or at least once a year.
Document in rope log
Inspect visually, by touch
Glass shards
Metal shavings
Splinters
Foreign objects

## Slide 23: Inspect kernmantle rope by applying slight tension and feeling for irregularities.
Soft spots
May signal core damage
If sheath damaged, core likely as well
If in doubt, remove from service
Other signs
Shape, weave
Smells
Discoloration
Roughness
Abrasions
Fuzziness
Some is normal
Remove from service if excessive
Courtesy of Shad Cooper/Wyoming
State Fire Marshal’s Office

## Slide 24: Untwist synthetic laid rope so each strand can be inspected.
1. Remove mildew
2. Clean Rope
3. Re-inspect
Look for:
Soft, crust, brittle spots
Stretching
Cuts, nicks, abrasions
Chemical abrasions
Dirt, grease, other flaws

## Slide 25: Remove natural fiber laid rope at manufacturer’s end of service period.
Overloaded
Ruptured fibers
Powdering between strands
Rot, mildew
Dark red, brown, black spots between strands
Sour, musty, acidic odor
Internal wear
Powdering between stands
(Cont.)

## Slide 26: Remove natural fiber laid rope at manufacturer’s end of service period.
Chemical Damage
Brittle, ruptured fibers
Dark red, brown spots
Salt incrustation
Swollen
Pulley, metallic devices
Rust spots
Reduced holding power
Heavy greasy material

## Slide 27: Ensure that rot does not spread to new rope.
1. Remove rope from service
2. Clean
3. Re-inspect
4. Dry, ventilate storage area before returning

## Slide 28: Inspect braided rope visually and by touch.
Exterior
Nicks, cuts, heat sears
Excessive, unusual fuzziness
Interior
Permanent mushy spots, deformities
Feel, squeeze surface

## Slide 29: Inspect braid-on-braid rope visually and by touch.
Heat sears, nicks, cuts
Lumps indicate core damage
Shrinking diameter may indicate break
Examine sheath for wear
If sheath slides on core:
Cut off end, remove excess, seal end

## Slide 30: Avoid abrasion and unnecessary wear while using any type of rope.
Chafing, dragging over rough surfaces
Constant vibration while in storage
Compression when stored tightly

## Slide 31: Avoid sharp angles and bends, which can reduce rope strength up to 50%.

## Slide 32: Protect rope ends from damage by taping or whipping them.

## Slide 33: Avoid exposing rope to sustained loads.
Synthetic fiber holds better than natural fiber
Can break below load limit after long periods of time
Never exceed load limit and never more than two days

## Slide 34: Avoid exposing rope to rust, which can weaken rope within one or two weeks.
Inspect extent
Remove from service, destroy
If stain is halfway through rope, strength may be reduced
If stain is minor, strength should not be diminished
Keep in service

## Slide 35: Prevent chemicals from coming into contact with any rope.
Natural fiber extremely vulnerable
Synthetic fiber not entirely resistant

## Slide 36: Reverse ends of the rope periodically to ensure an even wear.

## Slide 37: Do not walk on rope, which can weaken it by bruising and grinding dirt into the strands.

## Slide 38: Cleaning rope involves two basic steps.
1. Visually inspect for soil and other contamination
2. Use stiff brush to remove

## Slide 39: Do not use bleaches or strong cleaners on synthetic fiber rope; wash in warm water and mild detergent.
By hand
Rope washing device
Washing machine
Courtesy of Shad Cooper/Wyoming State Fire Marshal’s Office

## Slide 40: Dry synthetic fiber rope immediately after washing and rinsing.
Do:
Do Not:
Spread on hose drying rack
Suspend in hose tower
Coil loosely in hose dryer
Let dry in direct sunlight
Place near heat source

## Slide 41: Wipe or gently brush natural fiber rope, but do NOT use water.
Courtesy of Shad Cooper/Wyoming State Fire Marshal’s Office

## Slide 42: All life safety rope must be permanently identified with a rope log once purchased.
Mark ends
Print on label, seal to ends with liquid compound
Log is kept for working life
With unit number and service start date
(Cont.)

## Slide 43: All life safety rope must be permanently identified with a rope log once purchased.
Records dates every use, maintenance, inspection
Info helps determine when to remove from service
Log is kept in waterproof envelope in pocket on side of bag

## Slide 44: Follow these general guidelines for storing rope.
- Clean, dry, unheated area
- Freely circulating air
- Protect from weather, direct sunlight, chemicals, fumes, vapors
- Keep in separate compartment from fuels

## Slide 45: Storing ropes in a bag provides several advantages.
Easy to transport
Can be easily marked, with rope log attached
May be dropped, thrown to be deployed quickly
Protects against contamination, abrasion

## Slide 46: REVIEW QUESTION
Why would a rope need to be placed out of service?